## Slide 1
A Stress Test on 235U(n, f) in adjustment
with HCI and HMI benchmarks
WU Haicheng
China Nuclear Data Center(CNDC) China Institute of Atomic Energy(CIAE) P.O.Box 275-41,Beijing 102413, P.R.China
E-Mail: haicheng@ciae.ac.cn

## Slide 2
OUTLINE
Background
Method of stress test
3. Results and discussion
4. Summary

## Slide 3
Background
In SG33 benchmark exercise, adjusted results for ZPR6-7 F49/F25, ZPPR9 F28/F25 and F49/F25 reaction ratios are getting worse (decreased), which is suspected to be compensation errors caused by missing essential constraints of 235U(n,f) in 1~10keV energy region.
A stress test on 235U(n,f) to identify compensation errors was suggested with critical benchmarks sensitive to 235U(n,f) in 1~10keV region.
Notes: Pa, protactinium

## Slide 4
Case A (Sg33 benchmark exercise)
  11 isotope
    10B, 16O, 23Na, 52Cr, 56Fe, 58Ni, 235,238U, 239,240,241Pu
  8 Reactions
    (n, el), (n, inl), (n, disappearance),(n, f), Nu-total, Chi-p, Mu, Nu-delay.
  Covariance: JENDL-4.0
  20 Integral data
    JEZEBEL-Pu239 (keff, F28/F25,F49/F25, F37/F25), -Pu240 (keff), FLATTOP-Pu (keff, F28/F25, F37/F25), ZPR-6/7 (keff, F28/F25, F49/F25, C28/F25), -High Pu240 (keff), ZPPR-9 (keff, F28/F25, F49/F25, C28/F25, Na void reactivity (Step 3, 5)), JOYO Mk-I (keff) .
2. Method of stress test

## Slide 5
Case B (stress test 1)
  The same isotopes, reactions and covariances
  Integral data : + 1, HCI4.1 keff added.
    HCI4.1 is a k_inf benchmark with intermediate spectrum. The benchmark model is an infinity HEU moderated with graphite.
    HCI4.1 was design to provide a sensitivity test of 235U cross section over the energy range 10 eV to 10keV.
    Sensi. Coeffi. for 235U(n,f), 235U(n,γ), 10B(n,α) and 238U(n,γ) were used in calculation.
    Note: S.C. of HCI4.1 is not most sensitive benchmarks on 1~10keV region in ICSBEP.
Notes: the HCI4.1 experiment consisted of sample reactivity worth measurements. The measured reactivity worth for a number of fuel samples with varied boron content were interpolated to produce a boron/235U ratio which would yield a k_inf of unity.

## Slide 6
Case C (stress test 2)
  The same isotopes, reactions and covariances
  Integral data : + 2, HCI4.1 and HMI6.2 keff added.
    HMI6.2 is an intermediate-spectrum critical assembly with a graphite-HEU core surrounded by a copper reflector.
    Sensi. Coeffi. for 235U(n,f), 235U(n,γ), 10B(n,α) and 238U(n,γ) were used in calculation.

## Slide 7
Sensitivities to 235U(n,f) cross section
  Joyo MK-I is the only benchmark selected by SG33, whose keff is rather sensitive to 235U(n,f) XS in 1~10keV energy region than others.

## Slide 8
3. Results and discussion
Case A (20p) vs. Case B (21p)
  The improvement of keff values for SG33 cases are almost the same.

## Slide 9
Different constraint gives different direction of adjustment.
Reaction ratio were increased in case B instead of decrease
in case A.

## Slide 10
To improve the keff of HCI4.1, 235U(n,f) cross sections around 1 ~10keV were decreased in Case B instead of increased in case A.
Different constraints can even lead to contrary direction of adjustment.
Notes: In this case, the change of 235U(n,f) cross sections were driven by sensitivity of HCI004_1.

## Slide 11
To improve the keff of HCI4.1, 235U(n,γ) cross sections around 1 keV were increased in Case B instead of decreased in case A.

## Slide 12
To improve the keff of HCI4.1, 10B(n,α) cross section increased 0.1~0.6% < 1MeV.

## Slide 13
SVR results of ZPPR-9 were not change. Influence of 235U data change is compensated by others, such as
23 Na(n,el).

## Slide 14
Case A (20p) vs. Case B (21p) vs. Case C (22p)
  The improvement of keff values for SG33 cases are almost the same.
  The new adjusted keff of HCI4.1 get worse than case B.
Notes: In following figures, 21p indicate case B, 22p indicate case C.

## Slide 15
The adjusted reaction ratio in case C still a litter
higher than those in case A.

## Slide 16
To improve the keff of HCI4.1, 235U(n,f) cross sections were decreased between 0.5~2keV but increased between 2~10keV in Case C, which is not completely agree with case B.

## Slide 17
To keep the keff of HMI6.2 good, 235U(n,γ) cross sections around 1 keV were decreased 2% in Case C instead of increased 5% in case B.

## Slide 18
SVR results of ZPPR-9 were not change. Influence of 235U data change is still compensated by others, such as 23 Na(n,el). But change of 23 Na(n,el) get smaller.

## Slide 19
4. Comments
Missing essential constraints will lead to compensation errors.
  Different constraints can lead to different, even contrary adjustments for both integral and differential data.
To avoid compensation error and make adjusted nuclear data for general purpose, we need complete constraints.
  Global adjustment of library needs global constraints which we don’t have yet.
Even to obtained adjusted library not for general purpose, construct of constraints still needs to be careful.
  Different constraints (Such as benchmarks) give different library.

## Slide 20
Thank you for your attention !